## Slide 1
Project Work Progress Presentation - Review-2
SECURE AES-128 IMPLEMENTATION WITH
SIDE-CHANNEL ATTACK RESISTANCE
Branch: EL-VLSI (Electronics Engineering - VLSI Design and Technology)
Group No.: V-1
Under the Mentorship of:
Dr. Parveen Kumar
Assistant Professor
Presented By:
Ish Bhati (Roll No. 2300971730019)
Ishita Chaudhary (Roll No. 2300971730020)
Rishabh Verma (Roll No. 2300971730029)
Department of VLSI and Communication Technology
Galgotias College of Engineering and Technology, Gr. Noida(U.P.)

## Slide 2
Department of VLSI and Communication Technology
2
TITLE: Secure AES-128 Implementation with Side-Channel Attack Resistance
SDG GOALS (2-3 only):
• SDG 9: Industry, Innovation & Infrastructure (Target 9.5 & 9.c)
Fosters technological innovation and builds resilient digital infrastructure. Securing cryptographic hardware against side-channel power attacks protects smart grids, critical cyber-physical systems, and connected IoT infrastructure from physical eavesdropping and key extraction.
• SDG 16: Peace, Justice & Strong Institutions (Target 16.10)
Safeguards data privacy, institutional cybersecurity, and public trust. Prevents physical secret-key extraction from embedded cryptographic modules, securing sensitive governmental, financial, and industrial communication channels.
• SDG 12: Responsible Consumption & Production (Target 12.2 & 12.a)
Promotes silicon resource efficiency by optimizing the trade-off between side-channel security countermeasures and hardware overhead (minimizing LUT/FF area inflation and power dissipation).

## Slide 3
Department of VLSI and Communication Technology
3
TITLE: Secure AES-128 Implementation with Side-Channel Attack Resistance
PROGRAM OUTCOMES (POs) MAPPED (2-3 only):
• PO1 (Engineering Knowledge):
Applied Galois Field GF(2^8) composite field arithmetic, symmetric cryptography, and digital VLSI design principles to architect the 128-bit AES core.
• PO3 (Design/Development):
Engineered a first-order Boolean masked datapath (X' = X ⊕ M) with a glitch-resistant composite-field S-box and dynamic PRNG mask refresh balancing security and area overhead.
• PO5 (Modern Tool Usage):
Employed industry-standard EDA tools (AMD-Xilinx Vivado ML v2025.2, Verilog HDL) for RTL modeling, simulation, and logic synthesis.
PROGRAM SPECIFIC OUTCOMES (PSOs) MAPPED:
• PSO1 (VLSI System Design):
Demonstrated the capability to architect, model, and simulate secure hardware cryptographic subsystems using synthesizable Verilog HDL descriptions across modular datapath pipelines.
• PSO2 (EDA Tools & Verification):
Achieved proficiency in industry-grade FPGA synthesis, Static Timing Analysis (STA), clock constraint modeling, and hardware resource benchmarking targeting commercial AMD-Xilinx 7-series silicon.

## Slide 4
TABLE OF CONTENTS
Department of VLSI and Communication Technology
4
1. Introduction
Cryptographic background, side-channel power leakage & Boolean masking countermeasure.
2. Objectives
Core measurable milestones spanning RTL modeling, Vivado synthesis & TVLA assessment.
3. Proposed Improvement Over Existing Works
Systematic comparative benchmark against IEEE JSSC Base Paper (Kumar et al. 2023).
4. Methodology / Flowchart
Two-share masked datapath architecture & 4-stage EDA engineering design flow.
5. Work Done till Date and Results Obtained
NIST FIPS 197 verification, Vivado Artix-7 synthesis tables & verified simulation waveforms.
6. Project Implementation Budget Analysis
Cost breakdown table of academic EDA software vs. proposed physical prototyping.
7. Next Month Plan of Work
Action plan detailing on-chip PRNG integration, Canright S-Box & TVLA evaluation.
8. References
Formal IEEE bibliographical citations backing the theoretical & experimental framework.

## Slide 5
1. INTRODUCTION
Department of VLSI and Communication Technology
5
• Cryptographic Foundation (NIST FIPS 197):
– Advanced Encryption Standard (AES-128): is the standardized symmetric block cipher safeguarding critical communications in IoT, smart grids, defense systems, and cloud infrastructure.
– Iterative 10-Round Structure: transforms 128-bit plaintext blocks via SubBytes (non-linear S-box), ShiftRows (byte permutations), MixColumns (Galois matrix multiply), and AddRoundKey.
• Physical Hardware Vulnerability (Side-Channel Power Leakage):
– CMOS Switching Power Consumption: varies dynamically based on processed data: P_dyn = α · C_L · V_dd² · f. Attackers monitor supply current or EM emissions.
– DPA & CPA Attacks: exploit statistical correlation between physical power traces and intermediate Hamming Weight / Distance to extract master secret keys non-invasively within minutes.
• Hardware Countermeasure (First-Order Boolean Masking):
– Two-Share Secret Sharing: decorrelates power consumption from secret data by splitting sensitive states: X' = X ⊕ M, where M is a uniformly random mask.
– Datapath Synchronization: Linear layers (ShiftRows/MixColumns) process both shares in parallel; non-linear S-box requires dynamic mask refresh to eliminate first-order leakage.

## Slide 6
2. OBJECTIVES
Department of VLSI and Communication Technology
6
1. Synthesizable Baseline AES-128 RTL Datapath
Architect an iterative 128-bit AES encryption core in synthesizable Verilog HDL completing 10 rounds in 11 clock cycles. Verify 100% bit-accurate compliance against NIST FIPS 197 reference test vectors.
2. First-Order Boolean Masked Datapath Implementation
Implement a dual-share masking architecture (X' = X ⊕ M) across the datapath to break statistical correlation between internal switching power and intermediate cryptographic states.
3. Glitch-Resistant Masked S-Box & Dynamic Refresh Mechanism
Design a protected non-linear SubBytes transformation with dynamic PRNG mask-refreshing logic to counteract glitch-induced transient leakage and CMOS combinatorial hazards.
4. AMD-Xilinx Vivado Synthesis & Timing Closure Benchmarking
Synthesize both cores targeting the Artix-7 (xc7a35tcsg324-1) FPGA @ 100 MHz constraint in Vivado v2025.2. Extract exact Slice LUTs, Registers, Slack (WNS/WHS), and maximum frequency (Fmax).
5. Multi-Mode Verification & TVLA Security Framework
Execute behavioral, post-synthesis functional, and post-synthesis timing simulations. Lay the groundwork for statistical Welch's t-test / TVLA validation to guarantee leakage suppression (|t| < 4.5).

## Slide 7
3. PROPOSED IMPROVEMENT OVER EXISTING WORKS
Department of VLSI and Communication Technology
7
S. No | Base Paper(s) Publication Details | Base Paper(s) Major Findings | Base Paper(s) Limitations | Proposed Improvement over Existing Works | Expected Benefits
1. | R. Kumar, V. B. Suresh, S. Taneja, et al. (2023) IEEE Journal of Solid-State Circuits (JSSC) 'A 7-Gbps SCA-Resistant Multiplicative-Masked AES Engine in Intel 4 CMOS' [BASE PAPER] | • Multiplicative-masked AES engine in Intel 4 FinFET CMOS. • Dual-rail zero-value detection (ZVD) logic. • Achieved >34,000× MTD improvement against CPA/TVLA. | • Fabricated on Intel 4 custom silicon. • Requires specialized dual-rail custom transistor cells not synthesizable in academic FPGA RTL flows. | • Implemented a technology-independent synthesizable 1st-order Boolean masked architecture (X' = X ⊕ M) in Verilog HDL. • Mapped to standard FPGA Look-Up Tables (LUTs). | • 100% portable across standard commercial FPGAs (Artix-7). • Clean 100 MHz static timing closure (+1.54 ns slack), zero BRAM/DSP usage, and only 42.5% LUT overhead.
2. | D. Canright & L. Batina (2008) / F. Regazzoni et al. (2011) CARDIS / ACNS (Springer LNCS) 'FPGA Implementations of Masked AES: A Comparative Evaluation' | • Evaluated composite-field masked S-boxes on FPGA. • Highlighted trade-offs between slice utilization (LUTs/FFs), throughput, and SCA resistance. | • Unpipelined combinatorial inversion structures exhibit dynamic glitches and routing imbalances, causing transient 1st-order leakage. | • Iterative 10-round architecture with registered stage boundaries and synchronized two-share linear transformations. • Recombination isolated to final output register. | • Suppresses inter-round glitch propagation. • Stable 11-cycle execution latency with line-rate throughput (1.37 Gbps @ 118 MHz) and verifiable algorithmic security.

## Slide 8
4. METHODOLOGY/ FLOW CHART
Department of VLSI and Communication Technology
8
Figure 4.1: First-Order Boolean Masked AES-128 Iterative Datapath Architecture (Two-Share S' = P ⊕ M Pipeline)
Figure 4.2: Four-Stage EDA Engineering Design & Verification Flowchart from Verilog Modeling to Timing Closure

## Slide 9
5. WORK DONE TILL DATE AND RESULTS OBTAINED
Department of VLSI and Communication Technology
9
Figure 5.1: Synthesizable Verilog HDL Module Architecture (rtl/aes_128_masked_core.v)
Figure 5.2: AMD-Xilinx Vivado ML v2025.2 XSim Output: 100% NIST FIPS 197 Pass
Metric / Resource | Baseline | Masked | Overhead / Status
Slice LUTs | 1,350 | 1,924 | +42.5% (Util 9.25%)
Slice Registers (FF) | 393 | 524 | +33.3% (Util 1.26%)
Block RAM / DSP | 0 / 0 | 0 / 0 | 0% (100% Logic)
Timing Slack (WNS/WHS) | +4.16ns / +0.16ns | +1.54ns / +0.16ns | PASSED (Clean)
Max Frequency (Fmax) | 171.3 MHz | 118.2 MHz | >100 MHz (1.37 Gbps)
Table 5.1: Comparative Post-Synthesis Hardware Utilization on AMD-Xilinx Artix-7
Figure 5.3: Verified Post-Synthesis Timing Simulation Waveform (SDF Back-Annotated)

## Slide 10
6. PROJECT IMPLEMENTATION BUDGET ANALYSIS
Department of VLSI and Communication Technology
10
Note: Detailed cost breakdown of all aspects of project in tabular form, highlighting money spent till date vs. total proposed budget.
S. No | Item / Resource Description | Category | Specification / Tool | Cost Incurred (Spent) | Proposed Budget
1. | AMD-Xilinx Vivado ML Suite | EDA Software | ML Standard Edition v2025.2 (Free Academic) | ₹0.00 | ₹0.00
2. | RTL Simulator & Test Suite | EDA Software | Vivado XSim & Python 3.x Verification Suite | ₹0.00 | ₹0.00
3. | Development Workstation | Hardware | Department Laboratory PC (Synthesis Compute) | ₹0.00 | ₹0.00
4. | FPGA Development Board (Optional) | Hardware | AMD-Xilinx Artix-7 Evaluation Board (Basys 3) | ₹0.00 | ₹25,000.00
5. | RF Measurement Probes & Shunt | Hardware | Low-Noise SMA Coaxial & Power Shunt Probe | ₹0.00 | ₹3,500.00
TOTAL MONEY SPENT TILL REVIEW-2: ₹0.00
100% of milestones completed via software-based EDA simulation & synthesis.
TOTAL PROPOSED BUDGET (FUTURE REVISION): ₹28,500.00
Estimated for physical board procurement & laboratory RF measurement setup.

## Slide 11
7. NEXT MONTH PLAN OF WORK
Department of VLSI and Communication Technology
11
Task 1: Autonomous On-Chip PRNG Integration (Weeks 1–2)
Integrate an on-chip 128-bit hardware Pseudo-Random Number Generator (LFSR or Xorshift128+) into the AES datapath to generate and refresh independent random masks cycle-by-cycle without external testbench feed dependencies.
Task 2: Glitch-Resistant Composite-Field Canright S-Box (Weeks 3–4)
Replace memory-based S-boxes with Canright composite-field GF((2^4)^2) arithmetic to suppress dynamic CMOS glitch-induced transient power leakage during Galois field non-linear inversions.
Task 3: Power-Trace Simulation & Welch's t-test / TVLA (Weeks 5–6)
Extract cycle-accurate switching activity files (.vcd / .saif) from Vivado post-implementation timing simulations and compute Welch's t-test (Test Vector Leakage Assessment) statistics to verify |t| < 4.5.
Task 4: Physical FPGA Hardware Prototyping (Weeks 7–8)
Once a physical FPGA development board is procured in future revisions, integrate an on-chip communication interface (UART/AXI) to bridge host data and program the bitstream for laboratory board-level measurements.
Task 5: Final Dissertation, Documentation & Defense Preparation
Consolidate experimental synthesis benchmarks, complete the final B.Tech project dissertation, and prepare the project viva presentation and demonstration.

## Slide 12
8. REFERENCES
Department of VLSI and Communication Technology
12
[1] R. Kumar, V. B. Suresh, S. Taneja, M. A. Anders, S. Hsu, A. Agarwal, V. De, and S. K. Mathew, "A 7-Gbps SCA-Resistant Multiplicative-Masked AES Engine in Intel 4 CMOS," IEEE Journal of Solid-State Circuits, vol. 58, no. 4, pp. 1106–1116, Apr. 2023. [BASE PAPER]
[2] National Institute of Standards and Technology (NIST), "Advanced Encryption Standard (AES)," Federal Information Processing Standards Publication FIPS PUB 197, Nov. 2001 (Updated 2023).
[3] P. Kocher, J. Jaffe, and B. Jun, "Differential Power Analysis," in Advances in Cryptology — CRYPTO ’99, LNCS, vol. 1666, Springer, 1999, pp. 388–397.
[4] S. Chari, C. S. Jutla, J. R. Rao, and P. Rohatgi, "Towards Sound Approaches to Counteract Power-Analysis Attacks," in Advances in Cryptology — CRYPTO ’99, LNCS, vol. 1666, Springer, 1999, pp. 398–412.
[5] D. Canright and L. Batina, "A Very Compact Perfectly Masked S-Box for AES," in Applied Cryptography and Network Security (ACNS 2008), LNCS, vol. 5037, Springer, 2008, pp. 446–459.
[6] F. Regazzoni, Y. Wang, and F.-X. Standaert, "FPGA Implementations of Masked AES: A Comparative Evaluation," in CARDIS, Springer LNCS, 2011.
[7] G. T. Becker, J. Cooper, E. DeMulder, G. Goodwill, J. Jaffe, et al., "Test Vector Leakage Assessment (TVLA) Methodology in Practice," in Proc. International Cryptographic Module Conference (ICMC), 2013.

## Slide 13
Department of VLSI and Communication Technology
13
THANK YOU!
Questions & Answers
Open for Discussion, Suggestions & Feedback
Department of VLSI and Communication Technology Galgotias College of Engineering and Technology, Greater Noida (U.P.)